## Slide 1
NAME 338
SHIP DESIGN PROJECT AND PRESENTATION
BANGLADESH UNIVERSITY OF ENGINEERING AND TECHNOLOGY
Under the supervision of:
Dr. Md. Mashiur Rahaman
Professor
Department of Naval Architecture and Marine Engineering
BUET
Prepared by,
Noshin Tarannum Tasfia (1712002)
Rafid Imam (1712043)

## Slide 2
TABLE OF CONTENTS
Owner’s Requirement | 03
Route Specification | 04
Basis Ship Selection | 05
Principal Particulars Comparison between Basis Ship and Design Ship | 06
Principal Particulars Comparison between Preliminary and Final Design Ship | 07
Manning | 08
General Arrangement Plan | 09
Lines Plan | 10
Final Offset Table for Design Ship | 11
Hydrostatics Curves | 12
Scantling Calculation | 13
Midship Section | 16
Longitudinal Construction | 17
Page
Lacking From Third Presentation | 28
Achievements | 29
Rudder Calculation Summary | 30
Rudder Design | 31
Steering Gear Arrangement | 33
Propeller Design | 35
Propeller Cavitation Check | 36
Propeller Shaft Arrangement | 37
Engine Foundation Summary | 38
Design on Engine Foundation | 39
Trim Calculation | 41
Stability Calculation | 42
Resistance Calculation | 23
Power Calculation | 24
Engine and Gear Box Selection | 26
Shell Expansion | 18
Detailed Lightweight and Deadweight Calculation | 20
Page

## Slide 3
OWNER’S REQUIREMENT
Vessel Type: General Cargo
Route: Dhaka to Chittagong
Service Speed: 10 knot
Deadweight: 3000 tones

## Slide 4
Route: Dhaka to Chittagong
(Shadar Ghat to Chittagong Port)
Route Length: 304 km
(164 Nautical Miles)
ROUTE SPECIFICATION

## Slide 5
BASIS SHIP SELECTION
Length overall, | 82.56 m
Length between Perpendicular, | 79.29 m
Breadth, B | 16.00 m
Depth, D | 5.50 m
Draft, H | 4.10m
 | 0.859
Deadweight | 3200 tonnes
Speed | 10 knot
Displacement | 4526.83 tonnes
Class | IRS
 | 82.56 m
 | 79.29 m
Breadth, B | 16.00 m
Depth, D | 5.50 m
Draft, H | 4.10m
 | 0.859
Deadweight | 3200 tonnes
Speed | 10 knot
Displacement | 4526.83 tonnes
Class | IRS
M.V. ROKNOOR 32
Source: https://www.omeltd.com/projects/15

## Slide 6
DETERMINATION OF PRINCIPAL PARTICULARS OF DESIGN SHIP
From the Ratio of Basis Ship:
L/B = 4.956
B/H = 3.902
B/D = 2.909
H/B = 0.256
Applying Cubic Root Formula Length, = 77.942m
Now from the ratio of basis ship we get,
Breadth, B 15.728 m
Depth, D 5.500 m
Draft, H 4.100 m
Displacement 4317.350 tones

## Slide 7
DETERMINATION OF PRINCIPAL PARTICULARS OF DESIGN SHIP
Using Empirical Method For general cargo ship Length, L = = 78.620 m Breadth, B 15.865 m Depth, D 5.453 m Draft, H 4.065 m Displacement 4355.60 tones | Using Munro-Smith For a general Cargo Ship, Displacement 4400.000 tones Again, (page 18, method 3 ,ex-2.3) Length, L 78.886 m Breadth, B 15.918 m Depth, D 5.472 m Draft, H 4.079 m

## Slide 8
 | Using Basis Ship Ratio | Using Empirical Formula | Using formula from Munro Smith | Average dimensions
Length, L | 77.942 | 78.620 | 78.886 | 78.483
Breadth, B | 15.728 | 15.865 | 15.918 | 15.837
Depth, D | 5.500 | 5.453 | 5.472 | 5.475
Draft, H | 4.100 | 4.065 | 4.079 | 4.081
DETERMINATION OF PRINCIPAL PARTICULARS OF DESIGN SHIP
Comparison among different methods

## Slide 9
Principal Particulars of Design Ship
Length Overall, | 81.720 m
Length Between Perpendicular, | 78.483 m
Breadth, B | 15.837 m
Depth, D | 5.475 m
Draft, H | 4.081 m
Deadweight | 3000 tones
Displacement | 4357.200 tones
 | .859
 | .690
 | 81.720 m
 | 78.483 m
Breadth, B | 15.837 m
Depth, D | 5.475 m
Draft, H | 4.081 m
Deadweight | 3000 tones
Displacement | 4357.200 tones
 | .859
 | .690

## Slide 10
PRINCIPAL PARTICULARS COMPARISON BETWEEN BASIS SHIP AND DESIGN SHIP
Parameters | Basis Ship | Design Ship
Length Overall, | 82.56 m | 81.16 m
Length Between Perpendicular, | 79.29 m | 77.94 m
Breadth, B | 16.00 m | 15.72 m
Depth, D | 5.50 m | 5.41 m
Draft, H | 4.10 m | 3.59 m
Deadweight | 3200 tonnes | 3000 tonnes
Displacement | 4526.83 tonnes | 3776.00 tonnes
 | 0.859 | .859
 | 0.707 | .700
Parameters | Basis Ship | Design Ship
 | 82.56 m | 81.16 m
 | 79.29 m | 77.94 m
Breadth, B | 16.00 m | 15.72 m
Depth, D | 5.50 m | 5.41 m
Draft, H | 4.10 m | 3.59 m
Deadweight | 3200 tonnes | 3000 tonnes
Displacement | 4526.83 tonnes | 3776.00 tonnes
 | 0.859 | .859
 | 0.707 | .700

## Slide 11
POWER ESTIMATION & MANNING
=
We know,
Admiralty Coefficient, Ac =
For Basis ship and design Ship
Power of Basis Ship 1125 KW
So using the formula we can estimate the power of Design Ship = 1096 KW
1096 KW for two Engines. Thus 548 KW for each of them
Fuel Used : Diesel

## Slide 12
PRELIMINARY WEIGHT CALCULATION AND POWER ESTIMATION
Service Speed , V = 10 knot
= 18.5 km/h
Voyage distance , s = 164 nautical miles
Voyage time, t = 2 ∙ s / v =32.800 Hours
= 1.3667 Days
Endurance time = 4Days
= 96 Hours
Cargo Capacity (tones) = 2950 tones
Power of Basis Ship = 1125 KW
Admiralty Coefficient of Basis Ship : 243.2150866
Crew Member: 16
Engine Information
Model M26
BHP 548 KW each
SFC ≤ 213 gKW/h
SLOC ≤ 1.0 gKW/h
Source : Weichai Marine Engines

## Slide 13
PRELIMINARY WEIGHT CALCULATION AND POWER ESTIMATION
BHP ( Single Engine ) 548 kW
BHP = ( 2 ∙ 1 engine's BHP ) 1096 kW
SFC ( Single Engine ) 213 g/kW∙hr
SLOC ( Single Engine ) 0.8 g/kW∙hr
Constant Addition of Fuel 1.5 1.14-1.5
WHFO = SFC ∙ BHP ∙ Voyage time ∙ Constant Addition =11485.6416 kg
WDO = 20% of WHFO = 2297.12832 kg
WLO = SLOC ∙ BHP ∙ Voyage time ∙ Constant Addition =43.13856 kg
Fresh water consumption for
Crew = 20 kg per person per day=1280 kg
Bath & Laundry needs = 200 kg per person per day
=12800 kg
Cooking = 4 kg per person per day 256 kg
Machinery (Main Engine) ( 10 g/kW∙hr ) =1052.16 kg
Auxiliary needs = 20% of Main Engine= 210.432 kg
Reserve 5000 kg
Net Crew Weight = 75 kg ∙ Crew Member=1200 kg
Store & Provision = 10 kg per person per day=640kg
Net weight =36264.50048 kg= 36.2645 tonnes
Deadweight = Cargo capacity + Net Weight= 2986.2645tonnes
Displacement , Δ = Deadweight / =4340.5007 tonnes
PB = = 1094.0472 kW
PB per engine = 547.0236 kW
Iteration 1

## Slide 14
PRELIMINARY WEIGHT CALCULATION AND POWER ESTIMATION
BHP ( Single Engine ) 547.0236 kW
BHP = ( 2 ∙ 1 engine's BHP ) 1094.047165 kW
SFC ( Single Engine ) 211 g/kW∙hr
SLOC ( Single Engine ) 0.8 g/kW∙hr
Constant Addition of Fuel 1.5 1.14-1.5
WHFO = SFC ∙ BHP ∙ Voyage time ∙ Constant Addition =12557.1609 kg
WDO = 20% of WHFO= 2511.43218 kg
WLO = SLOC ∙ BHP ∙ Voyage time ∙ Constant Addition =47.61008871 kg
Fresh water consumption for Crew = 20 kg per person per day = 1280kg
Bath & Laundry needs = 200 kg per person per day =12800 kg
Cooking = 4 kg per person per day 256 kg
Machinery (Main Engine) ( 10 g/kW∙hr )= 1050.285278 kg
Auxiliary needs = 20% of Main Engine = 210.0570556 kg
Reserve= 5000 kg
Net Crew Weight = 75 kg ∙ Crew Member = 1200 kg
Store & Provision = 10 kg per person per day= 640 kg
Net weight = 37552.5455 kg
= 37.5525455 tonnes
Deadweight = Cargo capacity + Net Weight =2987.552545 tonnes
Displacement , Δ = Deadweight / =4342.372886 tonnes
PB = = 1094.384622 kW
PB per engine 547.1923109 kW
Iteration 2

## Slide 15
Iteration 3 | 546.969 KW
Iteration 4 | 546.968 KW
Iteration 5 | 546.968 KW
PRELIMINARY WEIGHT CALCULATION AND POWER ESTIMATION
Following the same path as before we got,
Preliminary Engine Power 547 KW each
Total of 1094 KW
Source: Ship Design Methodologies of Preliminary Design by Apostolos Papanikolaou

## Slide 16
PRELIMINARY GENERAL ARRANGEMENT PLAN
Determination of Number of Bulkheads
Distance between two bulkheads = .15L + 6.5
=18.27 m
So the Number of Bulkhead Stands = 4
Determination of Frame Spacing
Frame spacing = 450 + 2L
Framing System : Transverse Framing
Source: Inland Shipping Ordinance

## Slide 17
MANNING
Speed 10 knots
Owner | 1
1st Class Master | 1
2nd Class Master | 1
Sailor | 7
Inland Marine Engineer | 2
1st Class Driver | 1
Greaser | 3
Total | 16
Source: Inland Shipping Ordinance

## Slide 18
GENERAL ARRANGEMENT PLAN

## Slide 19
LINES PLAN

## Slide 20
FINAL OFFSET TABLE FOR DESIGN SHIP

## Slide 21
Water Plane area, Displacement, LCB, VCB calculation for WL - 1 |  |  |  |  |  |  |  |  |  |  |  | 
Water planes |  | 0 |  | 1 |  | 2 |  | Section Distance | 7.79 | WP Distance |  | 0.90
 | SM | 5 |  | 8 |  | -1 |  | Area products for sectional area | Sectional area below waterline | Volume Function | Levers | Moments about amidship
Section | SM | y0 | y x SM | y1 | y x SM | y2 | y x SM |  |  |  |  | 
0.00 | 0.50 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | -5.00 | 0.00
0.50 | 2.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | -4.50 | 0.00
1.00 | 1.00 | 0.00 | 0.00 | 0.00 | 0.00 | 6.26 | 6.26 | -6.26 | -0.94 | -0.94 | -4.00 | 3.75
1.50 | 2.00 | 0.00 | 0.00 | 7.16 | 14.33 | 7.68 | 15.35 | 49.63 | 7.42 | 14.84 | -3.50 | -51.94
2.00 | 1.50 | 6.21 | 9.31 | 7.79 | 11.68 | 7.85 | 11.78 | 85.49 | 12.78 | 19.17 | -3.00 | -57.51
3.00 | 4.00 | 6.50 | 26.00 | 7.85 | 31.39 | 7.86 | 31.46 | 87.42 | 13.07 | 52.27 | -2.00 | -104.55
4.00 | 2.00 | 6.50 | 13.00 | 7.85 | 15.70 | 7.86 | 15.73 | 87.42 | 13.07 | 26.14 | -1.00 | -26.14
5.00 | 4.00 | 6.50 | 26.00 | 7.85 | 31.39 | 7.86 | 31.46 | 87.42 | 13.07 | 52.27 | 0.00 | 0.00
6.00 | 2.00 | 6.50 | 13.00 | 7.85 | 15.70 | 7.86 | 15.73 | 87.42 | 13.07 | 26.14 | 1.00 | 26.14
7.00 | 4.00 | 6.50 | 26.00 | 7.85 | 31.39 | 7.86 | 31.46 | 87.42 | 13.07 | 52.27 | 2.00 | 104.55
8.00 | 1.50 | 5.92 | 8.88 | 7.84 | 11.76 | 7.86 | 11.80 | 84.48 | 12.63 | 18.94 | 3.00 | 56.83
8.50 | 2.00 | 4.72 | 9.44 | 7.79 | 15.57 | 7.84 | 15.69 | 78.05 | 11.67 | 23.34 | 3.50 | 81.68
9.00 | 1.00 | 2.50 | 2.50 | 6.90 | 6.90 | 7.12 | 7.12 | 60.62 | 9.06 | 9.06 | 4.00 | 36.25
9.50 | 2.00 | 2.48 | 4.96 | 4.44 | 8.88 | 4.73 | 9.47 | 43.19 | 6.46 | 12.91 | 4.50 | 58.11
10.00 | 0.50 | 0.00 | 0.00 | 0.00 | 0.00 | 1.02 | 0.51 | -1.02 | -0.15 | -0.08 | 5.00 | -0.38
Different totals |  | Sum of the area products of WP 0 | 139.09 | Sum of the area products of WP 1 | 194.69 | Sum of the area products of WP 2 | 203.79 | Summation of volume functions |  | 306.35 | Summation of moments | 126.79
Waterplane area |  | 722.75 |  | 1011.66 |  | 1058.94 |  |  |  |  |  | 
SM |  | 5.00 |  | 8.00 |  | -1.00 |  | VOLUME |  | 795.920 | LCB | 3.23
Volume products |  | 3613.74 |  | 8093.26 |  | -1058.94 |  | Summation of volume products | 10648.06 | VOLUME |  | 795.92
Levers |  | 0.00 |  | 1.00 |  | 2.00 |  |  |  |  |  | 
Monent about the keel |  | 0.00 |  | 8093.26 |  | -2117.89 |  | Summation of moments | 5975.38 | VCB |  | 0.50
Calculation for Waterline 01

## Slide 22
Water Plane area, Displacement, LCB, VCB calculation for WL - 2 |  |  |  |  |  |  |  |  |  |  |  | 
Water planes |  | 0 |  | 1 |  | 2 |  | Section Distance | 7.79 | WP Distance |  | 0.90
 | SM | 1 |  | 4 |  | 1 |  | Area products for sectional area | Sectional area below waterline | Volume Function | Levers | Moments about amidship
Section | SM | y0 | y x SM | y1 | y x SM | y2 | y x SM |  |  |  |  | 
0.00 | 0.50 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | -5.00 | 0.00
0.50 | 2.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | -4.50 | 0.00
1.00 | 1.00 | 0.00 | 0.00 | 0.00 | 0.00 | 6.26 | 6.26 | 6.26 | 3.75 | 3.75 | -4.00 | -14.98
1.50 | 2.00 | 0.00 | 0.00 | 7.16 | 14.33 | 7.68 | 15.35 | 36.33 | 21.72 | 43.45 | -3.50 | -152.07
2.00 | 1.50 | 6.21 | 9.31 | 7.79 | 11.68 | 7.85 | 11.78 | 45.21 | 27.03 | 40.55 | -3.00 | -121.65
3.00 | 4.00 | 6.50 | 26.00 | 7.85 | 31.39 | 7.86 | 31.46 | 45.75 | 27.36 | 109.44 | -2.00 | -218.88
4.00 | 2.00 | 6.50 | 13.00 | 7.85 | 15.70 | 7.86 | 15.73 | 45.75 | 27.36 | 54.72 | -1.00 | -54.72
5.00 | 4.00 | 6.50 | 26.00 | 7.85 | 31.39 | 7.86 | 31.46 | 45.75 | 27.36 | 109.44 | 0.00 | 0.00
6.00 | 2.00 | 6.50 | 13.00 | 7.85 | 15.70 | 7.86 | 15.73 | 45.75 | 27.36 | 54.72 | 1.00 | 54.72
7.00 | 4.00 | 6.50 | 26.00 | 7.85 | 31.39 | 7.86 | 31.46 | 45.75 | 27.36 | 109.44 | 2.00 | 218.88
8.00 | 1.50 | 5.92 | 8.88 | 7.84 | 11.76 | 7.86 | 11.80 | 45.16 | 27.00 | 40.50 | 3.00 | 121.51
8.50 | 2.00 | 4.72 | 9.44 | 7.79 | 15.57 | 7.84 | 15.69 | 43.71 | 26.14 | 52.28 | 3.50 | 182.98
9.00 | 1.00 | 2.50 | 2.50 | 6.90 | 6.90 | 7.12 | 7.12 | 37.23 | 22.27 | 22.27 | 4.00 | 89.06
9.50 | 2.00 | 2.48 | 4.96 | 4.44 | 8.88 | 4.73 | 9.47 | 24.97 | 14.93 | 29.87 | 4.50 | 134.41
10.00 | 0.50 | 0.00 | 0.00 | 0.00 | 0.00 | 1.02 | 0.51 | 1.02 | 0.61 | 0.31 | 5.00 | 1.53
Different totals |  | Sum of the area products of WP 0 | 139.09 | Sum of the area products of WP 1 | 194.69 | Sum of the area products of WP 2 | 203.79 | Summation of volume functions |  | 670.74 | Summation of moments | 240.79
Waterplane area |  | 722.75 |  | 1011.66 |  | 1058.94 |  |  |  |  |  | 
SM |  | 1.00 |  | 4.00 |  | 1.00 |  | VOLUME |  | 1742.62 | LCB | 2.80
Volume products |  | 722.75 |  | 4046.63 |  | 1058.94 |  | Summation of volume products | 5828.32 | VOLUME |  | 1742.62
Levers |  | 0.00 |  | 1.00 |  | 2.00 |  |  |  |  |  | 
Monent about the keel |  | 0.00 |  | 4046.63 |  | 2117.89 |  | Summation of moments | 6164.52 | VCB |  | 0.95
Calculation for Waterline 02

## Slide 23
Water Plane area, Displacement, LCB, VCB calculation for WL - 3 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Water planes |  | 0 |  | 1 |  | 2 |  | 3 |  | Section Distance | 7.79 | WP Distance |  | 0.90
 | SM | 1 |  | 3 |  | 3 |  | 1 |  | Area products for sectional area | Sectional area below waterline | Volume Function | Levers | Moments about amidship
Section | SM | y0 | y x SM | y1 | y x SM | y2 | y x SM | y3 | y x SM |  |  |  |  | 
0.00 | 0.50 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | -5.00 | 0.00
0.50 | 2.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 4.72 | 9.44 | 4.72 | 3.17 | 6.35 | -4.50 | -28.56
1.00 | 1.00 | 0.00 | 0.00 | 0.00 | 0.00 | 6.26 | 6.26 | 7.17 | 7.17 | 25.96 | 17.46 | 17.46 | -4.00 | -69.84
1.50 | 2.00 | 0.00 | 0.00 | 7.16 | 14.33 | 7.68 | 15.35 | 7.76 | 15.53 | 52.28 | 35.17 | 70.34 | -3.50 | -246.19
2.00 | 1.50 | 6.21 | 9.31 | 7.79 | 11.68 | 7.85 | 11.78 | 7.84 | 11.77 | 60.97 | 41.01 | 61.52 | -3.00 | -184.56
3.00 | 4.00 | 6.50 | 26.00 | 7.85 | 31.39 | 7.86 | 31.46 | 7.86 | 31.46 | 61.50 | 41.37 | 165.49 | -2.00 | -330.98
4.00 | 2.00 | 6.50 | 13.00 | 7.85 | 15.70 | 7.86 | 15.73 | 7.86 | 15.73 | 61.50 | 41.37 | 82.74 | -1.00 | -82.74
5.00 | 4.00 | 6.50 | 26.00 | 7.85 | 31.39 | 7.86 | 31.46 | 7.86 | 31.46 | 61.50 | 41.37 | 165.49 | 0.00 | 0.00
6.00 | 2.00 | 6.50 | 13.00 | 7.85 | 15.70 | 7.86 | 15.73 | 7.86 | 15.73 | 61.50 | 41.37 | 82.74 | 1.00 | 82.74
7.00 | 4.00 | 6.50 | 26.00 | 7.85 | 31.39 | 7.86 | 31.46 | 7.86 | 31.46 | 61.50 | 41.37 | 165.49 | 2.00 | 330.98
8.00 | 1.50 | 5.92 | 8.88 | 7.84 | 11.76 | 7.86 | 11.80 | 7.86 | 11.80 | 60.91 | 40.97 | 61.46 | 3.00 | 184.38
8.50 | 2.00 | 4.72 | 9.44 | 7.79 | 15.57 | 7.84 | 15.69 | 7.85 | 15.69 | 59.46 | 40.00 | 80.00 | 3.50 | 280.01
9.00 | 1.00 | 2.50 | 2.50 | 6.90 | 6.90 | 7.12 | 7.12 | 7.17 | 7.17 | 51.74 | 34.81 | 34.81 | 4.00 | 139.22
9.50 | 2.00 | 2.48 | 4.96 | 4.44 | 8.88 | 4.73 | 9.47 | 4.70 | 9.40 | 34.70 | 23.34 | 46.69 | 4.50 | 210.08
10.00 | 0.50 | 0.00 | 0.00 | 0.00 | 0.00 | 1.02 | 0.51 | 0.92 | 0.46 | 3.99 | 2.69 | 1.34 | 5.00 | 6.71
Different totals |  | Sum of the area products of WP 0 | 139.09 | Sum of the area products of WP 1 | 194.69 | Sum of the area products of WP 2 | 203.79 | Sum of the area products of WP 3 | 214.24 | Summation of volume functions |  | 1041.92 | Summation of moments | 291.25
Waterplane area |  | 722.75 |  | 1011.66 |  | 1058.94 |  | 1113.20 |  |  |  |  |  | 
SM |  | 1.00 |  | 3.00 |  | 3.00 |  | 1.00 |  | VOLUME |  | 2706.987 | LCB | 2.18
Volume products |  | 722.75 |  | 3034.97 |  | 3176.83 |  | 1113.20 |  | Summation of volume products | 8047.75 | VOLUME |  | 2706.99
Levers |  | 0.00 |  | 1.00 |  | 2.00 |  | 3.00 |  |  |  |  |  | 
Monent about the keel |  | 0.00 |  | 3034.97 |  | 6353.66 |  | 3339.60 |  | Summation of moments | 12728.23 | VCB |  | 1.42
Calculation for Waterline 03

## Slide 24
Water Plane area, Displacement, LCB, VCB calculation for WL - 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Water planes |  | 0 |  | 1 |  | 2 |  | 3 |  | 4 |  | Section Distance | 7.79 | WP Distance |  | 0.90
 | SM | 1 |  | 4 |  | 2 |  | 4 |  | 1 |  | Area products for sectional area | Sectional area below waterline | Volume Function | Levers | Moments about amidship
Section | SM | y0 | y x SM | y1 | y x SM | y2 | y x SM | y3 | y x SM | y4 | y x SM |  |  |  |  | 
0.00 | 0.50 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | -5.00 | 0.00
0.50 | 2.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 4.72 | 9.44 | 6.51 | 13.02 | 25.38 | 15.18 | 30.35 | -4.50 | -136.60
1.00 | 1.00 | 0.00 | 0.00 | 0.00 | 0.00 | 6.26 | 6.26 | 7.17 | 7.17 | 7.38 | 7.38 | 48.57 | 29.05 | 29.05 | -4.00 | -116.18
1.50 | 2.00 | 0.00 | 0.00 | 7.16 | 14.33 | 7.68 | 15.35 | 7.76 | 15.53 | 7.76 | 15.53 | 82.82 | 49.53 | 99.05 | -3.50 | -346.68
2.00 | 1.50 | 6.21 | 9.31 | 7.79 | 11.68 | 7.85 | 11.78 | 7.84 | 11.77 | 7.85 | 11.77 | 92.29 | 55.19 | 82.78 | -3.00 | -248.33
3.00 | 4.00 | 6.50 | 26.00 | 7.85 | 31.39 | 7.86 | 31.46 | 7.86 | 31.46 | 7.86 | 31.46 | 92.94 | 55.58 | 222.30 | -2.00 | -444.61
4.00 | 2.00 | 6.50 | 13.00 | 7.85 | 15.70 | 7.86 | 15.73 | 7.86 | 15.73 | 7.86 | 15.73 | 92.94 | 55.58 | 111.15 | -1.00 | -111.15
5.00 | 4.00 | 6.50 | 26.00 | 7.85 | 31.39 | 7.86 | 31.46 | 7.86 | 31.46 | 7.86 | 31.46 | 92.94 | 55.58 | 222.30 | 0.00 | 0.00
6.00 | 2.00 | 6.50 | 13.00 | 7.85 | 15.70 | 7.86 | 15.73 | 7.86 | 15.73 | 7.86 | 15.73 | 92.94 | 55.58 | 111.15 | 1.00 | 111.15
7.00 | 4.00 | 6.50 | 26.00 | 7.85 | 31.39 | 7.86 | 31.46 | 7.86 | 31.46 | 7.86 | 31.46 | 92.94 | 55.58 | 222.30 | 2.00 | 444.61
8.00 | 1.50 | 5.92 | 8.88 | 7.84 | 11.76 | 7.86 | 11.80 | 7.86 | 11.80 | 7.86 | 11.80 | 92.34 | 55.22 | 82.83 | 3.00 | 248.48
8.50 | 2.00 | 4.72 | 9.44 | 7.79 | 15.57 | 7.84 | 15.69 | 7.85 | 15.69 | 7.85 | 15.69 | 90.79 | 54.29 | 108.58 | 3.50 | 380.04
9.00 | 1.00 | 2.50 | 2.50 | 6.90 | 6.90 | 7.12 | 7.12 | 7.17 | 7.17 | 7.21 | 7.21 | 80.25 | 47.99 | 47.99 | 4.00 | 191.94
9.50 | 2.00 | 2.48 | 4.96 | 4.44 | 8.88 | 4.73 | 9.47 | 4.70 | 9.40 | 4.73 | 9.45 | 53.23 | 31.83 | 63.66 | 4.50 | 286.47
10.00 | 0.50 | 0.00 | 0.00 | 0.00 | 0.00 | 1.02 | 0.51 | 0.92 | 0.46 | 0.28 | 0.14 | 6.01 | 3.60 | 1.80 | 5.00 | 8.99
Different totals |  | Sum of the area products of WP 0 | 139.09 | Sum of the area products of WP 1 | 194.69 | Sum of the area products of WP 2 | 203.79 | Sum of the area products of WP 3 | 214.24 | Sum of the area products of WP 4 | 217.82 | Summation of volume functions |  | 1435.30 | Summation of moments | 268.14
Waterplane area |  | 722.75 |  | 1011.66 |  | 1058.94 |  | 1113.20 |  | 1131.83 |  |  |  |  |  | 
SM |  | 1.00 |  | 4.00 |  | 2.00 |  | 4.00 |  | 1.00 |  | VOLUME |  | 3728.994 | LCB | 1.46
Volume products |  | 722.75 |  | 4046.63 |  | 2117.89 |  | 4452.80 |  | 1131.83 |  | Summation of volume products | 12471.90 | VOLUME |  | 3728.99
Levers |  | 0.00 |  | 1.00 |  | 2.00 |  | 3.00 |  | 4.00 |  |  |  |  |  | 
Monent about the keel |  | 0.00 |  | 4046.63 |  | 4235.77 |  | 13358.40 |  | 4527.32 |  | Summation of moments | 26168.13 | VCB |  | 1.88
Calculation for Waterline 04

## Slide 25
BMT Calculation |  |  |  |  |  |  |  |  |  |  |  |  | 
Section | SM | Section Distance |  |  | 7.79 |  |  | Density of fresh water ( t/m3 ) |  |  | 1 |  | 
 |  | 1 |  |  | 2 |  |  | 3 |  |  | 4 |  | 
 |  | y1 | y3 | y3 ∙ SM | y2 | y3 | y3 ∙ SM | y3 | y3 | y3 ∙ SM | y4 | y3 | y3 ∙ SM
0.00 | 0.50 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
0.50 | 2.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 4.72 | 104.99 | 209.97 | 6.51 | 275.98 | 551.97
1.00 | 1.00 | 0.00 | 0.00 | 0.00 | 6.26 | 245.71 | 245.71 | 7.17 | 367.89 | 367.89 | 7.38 | 402.57 | 402.57
1.50 | 2.00 | 7.16 | 367.54 | 735.08 | 7.68 | 452.26 | 904.52 | 7.76 | 467.90 | 935.81 | 7.76 | 467.78 | 935.55
2.00 | 1.50 | 7.79 | 472.22 | 708.33 | 7.85 | 483.76 | 725.63 | 7.84 | 482.74 | 724.11 | 7.85 | 483.59 | 725.38
3.00 | 4.00 | 7.85 | 483.31 | 1933.25 | 7.86 | 486.33 | 1945.32 | 7.86 | 486.33 | 1945.32 | 7.86 | 486.33 | 1945.32
4.00 | 2.00 | 7.85 | 483.31 | 966.62 | 7.86 | 486.33 | 972.66 | 7.86 | 486.33 | 972.66 | 7.86 | 486.33 | 972.66
5.00 | 4.00 | 7.85 | 483.31 | 1933.25 | 7.86 | 486.33 | 1945.32 | 7.86 | 486.33 | 1945.32 | 7.86 | 486.33 | 1945.32
6.00 | 2.00 | 7.85 | 483.31 | 966.62 | 7.86 | 486.33 | 972.66 | 7.86 | 486.33 | 972.66 | 7.86 | 486.33 | 972.66
7.00 | 4.00 | 7.85 | 483.31 | 1933.25 | 7.86 | 486.33 | 1945.32 | 7.86 | 486.33 | 1945.32 | 7.86 | 486.33 | 1945.32
8.00 | 1.50 | 7.84 | 482.50 | 723.75 | 7.86 | 486.33 | 729.49 | 7.86 | 486.33 | 729.49 | 7.86 | 486.33 | 729.49
8.50 | 2.00 | 7.79 | 472.18 | 944.37 | 7.84 | 482.70 | 965.40 | 7.85 | 483.15 | 966.29 | 7.85 | 483.15 | 966.29
9.00 | 1.00 | 6.90 | 329.11 | 329.11 | 7.12 | 360.66 | 360.66 | 7.17 | 368.62 | 368.62 | 7.21 | 375.21 | 375.21
9.50 | 2.00 | 4.44 | 87.56 | 175.12 | 4.73 | 106.00 | 212.00 | 4.70 | 103.76 | 207.53 | 4.73 | 105.50 | 210.99
10.00 | 0.50 | 0.00 | 0.00 | 0.00 | 1.02 | 1.07 | 0.54 | 0.92 | 0.78 | 0.39 | 0.28 | 0.02 | 0.01
TOTALS |  |  |  | 11348.73 |  |  | 11925.22 |  |  | 12291.37 |  |  | 12678.74
Waterplane |  | 1 |  |  | 2 |  |  | 3 |  |  | 4 |  | 
Volume |  | 795.92 |  |  | 1742.62 |  |  | 2706.99 |  |  | 3728.99 |  | 
Δ |  | 795.92 |  |  | 1742.62 |  |  | 2706.99 |  |  | 3728.99 |  | 
Moment of Inertia, I |  | 19656.51 |  |  | 20655.02 |  |  | 21289.20 |  |  | 21960.14 |  | 
Transverse metacentric height, BMT |  | 24.70 |  |  | 11.85 |  |  | 7.86 |  |  | 5.89 |  | 
Calculation of BMT

## Slide 26
LCF and BML calculation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Section | SM | Section Distance |  |  |  | 7.79 |  | Length |  |  | 77.94 |  | Density of fresh water ( t/m3 ) |  |  |  | 1 | 
 |  | Levers from | 1 |  |  |  | 2 |  |  |  | 3 |  |  |  | 4 |  |  | 
 |  | amidsips (x) | y1 | y ∙ SM | ( y ∙ SM ) x | ( y ∙ SM ) x2 | y2 | y ∙ SM | ( y ∙ SM ) x | ( y ∙ SM ) x2 | y3 | y ∙ SM | ( y ∙ SM ) x | ( y ∙ SM ) x2 | y4 | y ∙ SM | ( y ∙ SM ) x | ( y ∙ SM ) x2
0.00 | 0.50 | -5.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
0.50 | 2.00 | -4.50 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 4.72 | 9.44 | -42.46 | 191.06 | 6.51 | 13.02 | -58.60 | 263.68
1.00 | 1.00 | -4.00 | 0.00 | 0.00 | 0.00 | 0.00 | 6.26 | 6.26 | -25.05 | 100.21 | 7.17 | 7.17 | -28.66 | 114.65 | 7.38 | 7.38 | -29.54 | 118.14
1.50 | 2.00 | -3.50 | 7.16 | 14.33 | -50.14 | 175.50 | 7.68 | 15.35 | -53.73 | 188.06 | 7.76 | 15.53 | -54.34 | 190.20 | 7.76 | 15.53 | -54.34 | 190.19
2.00 | 1.50 | -3.00 | 7.79 | 11.68 | -35.04 | 105.13 | 7.85 | 11.78 | -35.33 | 105.98 | 7.84 | 11.77 | -35.30 | 105.90 | 7.85 | 11.77 | -35.32 | 105.96
3.00 | 4.00 | -2.00 | 7.85 | 31.39 | -62.78 | 125.56 | 7.86 | 31.46 | -62.91 | 125.82 | 7.86 | 31.46 | -62.91 | 125.82 | 7.86 | 31.46 | -62.91 | 125.82
4.00 | 2.00 | -1.00 | 7.85 | 15.70 | -15.70 | 15.70 | 7.86 | 15.73 | -15.73 | 15.73 | 7.86 | 15.73 | -15.73 | 15.73 | 7.86 | 15.73 | -15.73 | 15.73
5.00 | 4.00 | 0.00 | 7.85 | 31.39 | 0.00 | 0.00 | 7.86 | 31.46 | 0.00 | 0.00 | 7.86 | 31.46 | 0.00 | 0.00 | 7.86 | 31.46 | 0.00 | 0.00
6.00 | 2.00 | 1.00 | 7.85 | 15.70 | 15.70 | 15.70 | 7.86 | 15.73 | 15.73 | 15.73 | 7.86 | 15.73 | 15.73 | 15.73 | 7.86 | 15.73 | 15.73 | 15.73
7.00 | 4.00 | 2.00 | 7.85 | 31.39 | 62.78 | 125.56 | 7.86 | 31.46 | 62.91 | 125.82 | 7.86 | 31.46 | 62.91 | 125.82 | 7.86 | 31.46 | 62.91 | 125.82
8.00 | 1.50 | 3.00 | 7.84 | 11.76 | 35.29 | 105.88 | 7.86 | 11.80 | 35.39 | 106.16 | 7.86 | 11.80 | 35.39 | 106.16 | 7.86 | 11.80 | 35.39 | 106.16
8.50 | 2.00 | 3.50 | 7.79 | 15.57 | 54.51 | 190.78 | 7.84 | 15.69 | 54.91 | 192.19 | 7.85 | 15.69 | 54.93 | 192.25 | 7.85 | 15.69 | 54.93 | 192.25
9.00 | 1.00 | 4.00 | 6.90 | 6.90 | 27.62 | 110.47 | 7.12 | 7.12 | 28.47 | 113.89 | 7.17 | 7.17 | 28.68 | 114.72 | 7.21 | 7.21 | 28.85 | 115.40
9.50 | 2.00 | 4.50 | 4.44 | 8.88 | 39.96 | 179.84 | 4.73 | 9.47 | 42.59 | 191.67 | 4.70 | 9.40 | 42.29 | 190.31 | 4.73 | 9.45 | 42.53 | 191.37
10.00 | 0.50 | 5.00 | 0.00 | 0.00 | 0.00 | 0.00 | 1.02 | 0.51 | 2.56 | 12.80 | 0.92 | 0.46 | 2.30 | 11.51 | 0.28 | 0.14 | 0.70 | 3.52
TOTALS |  |  |  | 194.69 | 72.20 | 1150.11 |  | 203.79 | 49.81 | 1294.07 |  | 214.24 | 2.83 | 1499.87 |  | 217.82 | -15.40 | 1569.78
 |  |  | 1 |  |  |  | 2 |  |  |  | 3 |  |  |  | 4 |  |  | 
Volume |  |  | 795.92 |  |  |  | 1742.62 |  |  |  | 2706.99 |  |  |  | 3728.99 |  |  | 
Water plane Area |  |  | 1011.66 |  |  |  | 1058.94 |  |  |  | 1113.20 |  |  |  | 1131.83 |  |  | 
TPC |  |  | 10.12 |  |  |  | 10.59 |  |  |  | 11.13 |  |  |  | 11.32 |  |  | 
LCF from Amidship |  |  | 2.89 |  |  |  | 1.91 |  |  |  | 0.10 |  |  |  | -0.55 |  |  | 
LCF from Aft |  |  | 37.39 |  |  |  | 36.41 |  |  |  | 34.60 |  |  |  | 33.95 |  |  | 
Moment of inertia about the amidship |  |  | 363048.14 |  |  |  | 408488.47 |  |  |  | 473452.44 |  |  |  | 495519.86 |  |  | 
Moment of inertia about the LCF |  |  | 354596.18 |  |  |  | 404644.87 |  |  |  | 473440.67 |  |  |  | 495176.34 |  |  | 
Longitudinal Metacenter BML |  |  | 445.52 |  |  |  | 232.20 |  |  |  | 174.90 |  |  |  | 132.79 |  |  | 
Δ |  |  | 795.92 |  |  |  | 1742.62 |  |  |  | 2706.99 |  |  |  | 3728.99 |  |  | 
MCT 1 cm |  |  | 45.49 |  |  |  | 51.92 |  |  |  | 60.74 |  |  |  | 63.53 |  |  | 
Calculation of LCF and BML

## Slide 27
WL | WL Height (m) | Displacement (tonnes) | VCB (m) | LCB (m) | TPC | BMT (m) | BML (m) | LCF form aft(m) | MCTC
1 | 0.90 | 795.41 | 0.50 | 3.23 | 10.12 | 24.71 | 445.80 | 37.39 | 45.49
2 | 1.79 | 1741.51 | 0.95 | 2.80 | 10.59 | 11.86 | 232.35 | 36.41 | 51.92
3 | 2.69 | 2705.26 | 1.42 | 2.18 | 11.13 | 7.87 | 175.01 | 34.60 | 60.74
4 | 3.59 | 3750.61 | 1.88 | 1.46 | 11.32 | 5.89 | 132.88 | 33.95 | 63.53
HYDROSTATICS CALCULATION
CB | CM | CP | CWP
0.72 | 0.93 | 0.78 | 0.83
0.79 | 0.97 | 0.82 | 0.86
0.82 | 0.98 | 0.84 | 0.91
0.85 | 0.98 | 0.86 | 0.92

## Slide 28
FINAL HYDROSTATICS CURVES FOR DESIGN SHIP
Chart: 
| 0.50335584166342517 | 0.94871528536536431 | 1.4186457722293966 | 1.8820039327750695
VCB | 0.89698 | 1.794 | 2.6909 | 3.5879
LCB | 0.89698 | 1.794 | 2.6909 | 3.5879
Displacement (*1000 tonnes) | 0.89698 | 1.794 | 2.6909 | 3.5879
TPC (*10) | 0.89698 | 1.794 | 2.6909 | 3.5879
BMT (*10) | 0.89698 | 1.794 | 2.6909 | 3.5879
BML (*100) | 0.89698 | 1.794 | 2.6909 | 3.5879
LCF (*10 m) | 0.89698 | 1.794 | 2.6909 | 3.5879
MCTC (*10) | 0.89698 | 1.794 | 2.6909 | 3.5879
Cb | 0.89698 | 1.794 | 2.6909 | 3.5879
Cm | 0.89698 | 1.794 | 2.6909 | 3.5879
Cp | 0.89698 | 1.794 | 2.6909 | 3.5879
Cwp | 0.89698 | 1.794 | 2.6909 | 3.5879

## Slide 29
Scantling
Parameters | Source
Material STRUCTURAL STEEL Material Factor, K = 1 Minimum Yield stress 235 N/mm2 Tensile Strength 400-490 N/mm2 | IRS; Part 3; Section 1.2; Chapter 2
Corrosion Addition Thickness, tc = 2 mm | IRS; Part 3; Section 2.1 ; Chapter 3
Frame Spacing 650 mm Web Frame Spacing 2600 mm | IRS; Part 3; Section 1.3.1 ; Chapter 3
For overall Scantling Process we followed the following Rulebooks
IRS Rules for Inland Waterways Vessel 2021
IRS Rules for Bulk Cargo Carriers 2021
Inland Shipping Ordinance
Consteel 2006

## Slide 30
PLATE | THICKNESS
Bottom Plate Thickness | 10 mm
Keel Plate Thickness | 11 mm
Inner Bottom Thickness | 9 mm
Floor Thickness | 9 mm
Side Shell Plating | 10 mm
Deck Plating ( Strength and Forecastle Deck) | 9 mm
Deck plating ( Other Deck) | 8 mm
Bulkhead Thickness ( Watertight Bulkhead) | 6 mm
Bulkhead Thickness (Tank and Collision Bulkhead) | 7 mm
Bulwark Thickness | 6 mm
SCANTLING

## Slide 31
PLATE | THICKNESS
Superstructure Thickness (Upper tier) | 5 mm
Superstructure Thickness Lower Tier) | 6 mm
Hatch Coaming Thickness ( Strength and Forecastle deck) | 9 mm
Hatch Coaming Thickness ( Others ) | 8 mm
Hatch Cover Thickness | 9 mm
Machinery Casing Thickness | 4 mm
Machinery Casing ( Bottom floor ) | 9 mm
Sheerstrake Thickness | 11 mm
Bilge Plate Thickness | 10 mm
SCANTLING

## Slide 32
STRUCTURAL MEMBERS | 
Center Girder | T-800×150×9
Side Girder | T-800×150×9
Floor | T-800×150×9
Side Web Frame | T-350×175×13
Side Frame | L-130×130×12
Side Stringers | T-350×175×13
Deck Girders | T-200×12, 150×8
Deck Web beam | T-125×65×9
Bulkhead Stiffeners | L-100×100×12
Bulkhead Girders | L-200×200×14
Superstructure Stiffeners | L-80×80×8
Girder(Machinery Space) | T-800×150×9
Web Frame(Machinery Space) | T-350×175×13
Hatch Cover Stiffeners and Girders | T-150×9, 100×6
SCANTLING

## Slide 33
MIDSHIP SECTION

## Slide 34
LONGITUDINAL CONSTRUCTION

## Slide 35
LONGITUDINAL CONSTRUCTION

## Slide 36
SHELL EXPANSION

## Slide 37
RESISTANCE CALCULATION BY HOLTROP AND MENNEN’S METHOD
Speed of our Ship , V=5.14 ms-1
Froude No=0.1845
Reynold’s No= 4.06×108
Resistance Components
Frictional Resistance, RF | 35.6 kN
Wave-Making Resistance, RW | 10.5 kN
Appendage Resistance , RAPP | 1.64 kN
Model Ship Correlation Resistance , RA | 11.7 kN
Air Resistance , RAA | 12.1 kN
Total Resistance, RT | 90 kN
Total Resistance Co-efficient, CT | 4.32×10-3

## Slide 38
POWER CALCULATION
Efficiencies and QPC Calculation
Taylor Wake Fraction , wT = 0.26
Thrust Deduction Factor , t = 0.22
Hull Efficiency , nH = 1.057
Relative Rotative Efficiency, nR = 1.028
QPC, Open Water Efficiency and Propeller RPM
 | Method 1 ( BP- Delta Chart) | Method 2 (KT and KQ)
QPC | 0.475 | 0.478
Propeller Open Water Efficiency, nO | 0.44 | 0.446
Propeller RPM | 325 | 329

## Slide 39
POWER CALCULATION
Total resistance | RT | RF+ RAPP + Rw + RA + RAA | 90 | kN
Effective Power | PE | RT*V | 460.52 | kW
QPC |  |  | 0.47 | 
Delivered Power | PD |  | 969.66 | kW
Shaft Efficiency | nS |  | 0.95 | 
Shaft Power | PS |  | 1020.69 | kW
 |  | Transmission line loss 5% for transmission via gear box |  | 
Engine power |  |  | 1074.41 | kW
Brake Power | Pb | (85% MCR),Considering 15% sea margin | 1200.81 | kW
Total installed power | PI | (100% MCR) | 1412.72 | kW
 |  |  | 710*2 | kW

## Slide 40
ENGINE SELECTION
We finally considered Two Engines of 710 kW or 950 HP
Engine Specifications
Model No: XCW6200ZC-1 (Ref. Marine Propulsion Engine , Weichai Catalogue)
Engine Power : 720 kW or 969 HP
Engine RPM : 1000
Net Weight : 6300 kg
Mechanical Pump Bore and stroke:200×270 mm
Displacement : 50.89 L
Min Fuel Consumption : 200g/kW-h
Dimension: L-2828 mm, W-1726 mm, H-2412mm, H*-2000 mm

## Slide 41
GEAR BOX SELECTION
Marine Gear Box Specifications
Model: WHG120 (Ref. Marine Propulsion Engine , Weichai Catalogue)
Input Speed: 750-2000 RPM
Gear Ratio : 3.03
Net Weight: 120 kg
Dimension : 792 mm× 609 mm× 736 mm

## Slide 42
LACKINGS FROM THIRD PRESENTATION
Incomplete Rudder Design & Steering Arrangement
Incomplete Propeller Design
Incomplete Trim Calculation
Incomplete Stability Calculation
Incomplete Engine Foundation scantling, Design of Engine Foundation

## Slide 43
ACHIEVEMENTS
Stability Calculation
Rudder Design and Steering Arrangement
Propeller Design & Shaft Arrangement
Design of Engine Foundation
Trim Calculation

## Slide 44
RUDDER CALCULATION SUMMARY
ITEM | VALUES
Area of a Single Rudder | 2.98 m2
Rudder Force | 60.40 kN
Rudder Torque | 21.20 kN-m
Rudder Stock Diameter | 100 mm
Rudder Coupling Bolt Diameter | 25 mm
Rudder Coupling Flange Thickness | 25 mm
Rudder Pintle Thickness | 8 mm
Rudder Pintle Diameter | 55 mm
Rudder Plate Thickness | 8 mm
Rudder Web Plate Thickness | 7 mm
Rudder Horizontal Frame Spacing | 560 mm
Rudder Vertical Frame Spacing | 830 mm
Profile | NACA -0020

## Slide 45
RUDDER DESIGN

## Slide 46
RUDDER DESIGN

## Slide 47
STEERING GEAR ARRANGEMENT
Working Torque for Steering Gear 25.5 kN-m
Steering Gear Model -7093- B20 ( Ref. Kobelt Electro-Hydraulic Steering Gear Catalogue)

## Slide 48
STEERING GEAR ARRANGEMENT
CL
Steering Arrangement (Plan View)

## Slide 49
Propeller Diameter at Behind Condition: 2.09 m
Propeller Diameter at open water Condition: 2.15 m
Blade Area Ratio: 0.55
Number of Blades: 3
Pitch-Diameter Ratio: 0.64
PROPELLER DESIGN

## Slide 50
PROPELLER CAVITATION CHECK
Local Cavitation Number , σ0.7 = 0.41
Mean Thrust Loading Coefficient , τc = 0.16

## Slide 51
PROPELLER SHAFT ARRANGEMENT
Diameter of Propeller Shaft 150 mm
Shaft Arrangement

## Slide 52
ENGINE FOUNDATION SCANTLING
ITEM | DIMENSION
Top Plate Area | 105.20 cm2
Top Plate Width | 450 mm
Top Plate Thickness | 25 mm
Girder Web Thickness | 12 mm
Floor Web Thickness | 9 mm
Floor Depth | 800 mm
Bracket Thickness | 7 mm
Foundation Bolt Diameter | 30 mm

## Slide 53
DESIGN OF ENGINE FOUNDATION

## Slide 54
DESIGN OF ENGINE FOUNDATION

## Slide 55
Total Weight of plates | 418.98 tonnes
Total weight of structural and stiffening members | 154.04 tonnes
Total Steel weight (considering 10% scrap) | 630.20 tonnes
Machinery weight | 45.61 tonnes
Wood and Outfit Weight | 12.60 tonnes
Lightweight | 688.55 tonnes
DETAILED LIGHTWEIGHT AND DEADWEIGHT CALCULATION

## Slide 56
Capacity of the Cargo Holds | 2898.86 tonnes
Capacity of Fresh Water Tank | 15.00 tonnes
Capacity of Fuel Oil Reserve Tank | 9.77 tonnes
Capacity of Lubricating Oil Reserve Tank | 0.06 tonnes
Capacity of Backward Ballast Water Tank | 160.19 tonnes
Crew weight | 1.12 tonnes
Provision | 0.80 tonnes
Deadweight | 3087.21 tonnes
DETAILED LIGHTWEIGHT AND DEADWEIGHT CALCULATION

## Slide 57
Lightweight | 688.55 tonnes
Deadweight | 3087.21 tonnes
Displacement | 3776.00 tonnes
Preliminary calculated deadweight was 3000 tonnes
Preliminary calculated displacement was 4243.90 tonnes
DETAILED LIGHTWEIGHT AND DEADWEIGHT CALCULATION

## Slide 58
TRIM CALCULATION AT FULL LOADED DEPARTURE CONDITION
LCG 0.40 m fwd from midship
LCB 1.45 fwd of Midship
LCF -.55 Fwd
MCTC 63.53
Displacement 3776 tonnes
Change in trim -62.75 cm
Change in draught at aft perpendicular -30.93 cm
Change in draught at fore perpendicular -31.82 cm
Final draft fwd. | 3.27 m
Final draft aft | 3.89 m
Trim by Stern

## Slide 59
Principal Particulars Comparison between Preliminary and Final Design Ship
Parameters | Final Design Ship | Preliminary Design Ship
Length Overall, | 81.16 m | 81.16 m
Length Between Perpendicular, | 77.94 m | 77.94 m
Breadth, B | 15.72 m | 15.72 m
Depth, D | 5.41 m | 5.41 m
Draft, H | 3.59 m | 4.03 m
Deadweight | 3000 tonnes | 3000 tonnes
Displacement | 3776.00 tonnes | 4243.90 tones
 | 0.859 | 0.859
 | 0.70 | 0.70
Parameters | Final Design Ship | Preliminary Design Ship
 | 81.16 m | 81.16 m
 | 77.94 m | 77.94 m
Breadth, B | 15.72 m | 15.72 m
Depth, D | 5.41 m | 5.41 m
Draft, H | 3.59 m | 4.03 m
Deadweight | 3000 tonnes | 3000 tonnes
Displacement | 3776.00 tonnes | 4243.90 tones
 | 0.859 | 0.859
 | 0.70 | 0.70

## Slide 60
Properties | IMO value | Lightship Condition
Area up to 30 degree (m-rad) | ≥ 0.055 | 1.405
Area up to 40˚ (m-rad) | ≥ 0.09 | 2.160
Area up to 30˚ - 40˚ (m-rad) | ≥ 0.03 | 0.755
GZ at 30 degree (m) | ≥ 0.2 | 4.901
Max. GZ at (degree) | ≥ 30 (preferable) but not ≤ 25 | 47.000
Initial Metacentric Height (m) | Should not be ≤ 0.15 | 10.800
STABILITY IN LIGHTSHIP CONDITION
PASS
PASS
PASS
PASS
PASS
PASS
Chart: Lightweight Condition GZ vs Angle of Heel
| 0 | 15 | 30 | 45 | 60 | 75 | 90
Lightweight GZ(m) | 0 | 2.7993 | 4.9006 | 6.5888 | 5.4332 | 2.3882 | -1.4651
57.3degree | 11 | 0
Lightship Condition |  |  | 
 | Capacity (tonnes) | vcg(from keel) (m) | Vcg moment (tonnes-m)
Cargo Hold1 | 0.00 | 3.09 | 0.00
Cargo Hold2 | 0.00 | 3.09 | 0.00
Lightweight | 688.97 | 3.66 | 2518.75
FWT(both) | 0.00 | 4.10 | 0.00
FORT | 0.00 | 3.90 | 0.00
LORT | 0.00 | 3.90 | 0.00
FOST*2 | 0.00 | 3.90 | 0.00
B.BWT | 0.00 | 2.80 | 0.00
Total Capacity | 688.97 | VCG | 3.66 m

## Slide 61
Properties | IMO value
Area up to 30 degree (m-rad) | ≥ 0.055
Area up to 40˚ (m-rad) | ≥ 0.09
Area up to 30˚ - 40˚ (m-rad) | ≥ 0.03
GZ at 30 degree (m) | ≥ 0.2
Max. GZ at (degree) | ≥ 30 (preferable) but not ≤ 25
Initial Metacentric Height (m) | Should not be ≤ 0.15
Fully Loaded Condition | 
0.609 | PASS
0.925 | PASS
0.316 | PASS
2.179 | PASS
42.000 | PASS
4.500 | PASS
STABILITY IN FULLY LOADED DEPARTURE CONDITION
Chart: Fully Loaded Condition GZ vs Angle of Heel
| 0 | 15 | 30 | 45 | 60 | 75 | 90
Fully Loaded Condition GZ(m) | 0 | 1.2 | 2.179 | 2.5103 | 1.7863 | 0.81824 | -0.52046
"57degree 2" | 6 | 0
Fully Loaded Departure Condition |  |  | 
 | Capacity (tonnes) | vcg(from keel) (m) | Vcg moment (tonnes-m)
Cargo Hold1 | 937.60 | 3.09 | 2897.18
Cargo Hold2 | 1965.26 | 3.09 | 6072.67
Lightweight | 688.55 | 3.72 | 2562.93
FWT(both) | 11.25 | 4.10 | 46.13
FORT | 9.77 | 3.90 | 38.12
LORT | 0.07 | 3.90 | 2.56
FOST*2 | 1.93 | 3.90 | 7.52
B.BWT | 160.19 | 2.80 | 448.54
Total Capacity | 3774.62 | VCG | 3.20 m

## Slide 62
Properties | IMO value | Ballast in Departure Condition | 
Area up to 30 degree (m-rad) | ≥ 0.055 | 1.1958 | PASS
Area up to 40˚ (m-rad) | ≥ 0.09 | 5.3890 | PASS
Area up to 30˚ - 40˚ (m-rad) | ≥ 0.03 | 4.1932 | PASS
GZ at 30 degree (m) | ≥ 0.2 | 3.9968 | PASS
Max. GZ at (degree) | ≥ 30 (preferable) but not ≤ 25 | 44 | PASS
Initial Metacentric Height (m) | Should not be ≤ 0.15 | 9.2 | PASS
STABILITY IN BALLAST IN DEPARTURE CONDITION
Chart: GZ vs Angle of Heel
| 0 | 15 | 30 | 45 | 60 | 75 | 90
GZ | 0 | 2.4266 | 3.9968 | 5.0098 | 4.5376 | 3.039 | -0.16641
57.3degree | 0 | 30
In Ballast in Departure Condition |  |  | 
 | Capacity (tonnes) | vcg(from keel) (m) | Vcg moment (tonnes-m)
Cargo Hold1 | 0.00 | 3.09 | 0.00
Cargo Hold2 | 0.00 | 3.09 | 0.00
Lightweight | 688.97 | 3.66 | 2518.75
FWT(both) | 15.00 | 4.10 | 46.13
FORT | 9.77 | 3.90 | 38.12
LORT | 0.07 | 3.90 | 2.56
FOST*2 | 1.93 | 3.90 | 7.52
B.BWT | 135.19 | 2.80 | 448.54
FPT | 191.44 | 3.28 | 627.91
FBWT | 190.74 | 2.75 | 524.54
BBWT | 81.35 | 4.23 | 344.11
DBT1 | 285.62 | 0.44 | 125.67
DBT2 | 563.36 | 0.44 | 247.88
APT | 130.06 | 4.76 | 619.09
Total Capacity | 2293.50 | VCG | 2.42 m

## Slide 63
THANK YOU